## Slide 1: ENERGY EFFICIENT 1-BIT APPROXIMATE FULL ADDERs using cntfet
Batch -1
Under the Guidance of Submitted by :-
Dr . M. Sarada G. Apurupa - 181FA05089
Professor P. Sai Krishna - 181FA05114
IV-ECE

## Slide 2: CONTENTS
Objective
Introduction
Existing Approximate Adder Circuits
Proposed Approximate Adder Circuits
Applications:
  4-bit Ripple Carry Adder Circuit
  2*4 Multiplier
Results
Conclusion
References
Publications

## Slide 3: Objectives
The objectives of energy efficient 1-bit approximate full adders using CNTFET are
To design the approximate full adder
To reduce the number of transistors
To reduce the power consumption and delay
To implement RCA and 2*4 multiplier using the proposed approximate adder

## Slide 4: INTRODUCTION
Approximate Computing is used to trade off the strict computing correctness of conventional full adder for better performance and energy efficiency of the digital computer system.
Approximate adders allow operating in parallel for high speed and energy efficiency with an existing chance of incorrect results.
Approximate Adders are mainly used for Image processing, Audio, Video Processing, and Machine learning applications.
The Carbon Nanotube Field Effect Transistor (CNFET) is used widely in nanotechnologies in place of MOSFETs. These comprise of two types P- type CNFET and n-type CNFET.
The CNTFETs are one-atom-thick layer graphene tubes that are transformed into cylindrical pipes. As compared to MOSFETs switching speed is high for CNTFETs.

## Slide 5: Cont..
Due to this factor, the Power dissipation is low for CNFET circuits than for MOSFET circuits. CNTFETs provide the opportunity to control the threshold voltage by changing the diameter of CNT, or chirality vector.
Carbon nanotubes are composed of tubular graphite plates that are based on the chirality vector C = ma1 + na2 where a1 and a2 are the unit vectors of the graphite plate, and the chirality (m, n) determines how the CNTs twist.
Fig.1: Structure CNTFET

## Slide 6: Cont..
Fig.2:Approximate Computing
6

## Slide 7: Exact Full Adder Circuit
No. of transistors: 24
Fig.3: Exact Full Adder
A | B | Cin | SUM | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
[1] Ghorbani, Ali & Ghorbani, Ghazaleh. (2014). Energy Efficient Full Adder Cell Design With Using Carbon Nanotube Field Effect Transistors In 32 Nanometer Technology. International Journal of VLSI Design & Communication Systems. 5. 10.5121/vlsic.2014.5501.
Expression:
SUM = ABC+ A ++ C
Cout =AB+BC+CA
Truth table of Exact Full Adder
7

## Slide 8: Existing Approximate Adder Circuits
Fig.4: Approximate Adder-1
A | B | C | Sum | Carry
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 0 | 1
[2]:M. Ramasamy, G. Narmadha and S. Deivasigamani, “Carry based approximate full adder for low power approximate computing,” 7th International Conference on Smart Computing & Communications (ICSCC), pp. 1-4, 2019.
No. of transistors : 14
Expression:
Sum =~Carry
Carry =(A. B)+C
Carry
Sum
Vdd
A
B
A
B
GND
Vdd
C
C
GND
Vdd
GND
Vdd
GND
Vdd
GND
Truth Table for AA1
Approximate Adder 1

## Slide 9: Approximate Adder 2
Fig.5: Approximate Adder-2
A | B | C | Sum | Carry
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 0 | 1
No. of transistors : 14
Expression:
Sum =~Carry
Carry =(B. C)+A
[2] M. Ramasamy, G. Narmadha and S. Deivasigamani, “Carry based approximate full adder for low power approximate computing,” 7th International Conference on Smart Computing & Communications (ICSCC), pp. 1-4, 2019.
Carry
Sum
Vdd
B
C
B
C
GND
Vdd
A
A
GND
Vdd
GND
Vdd
GND
Vdd
GND
Truth Table for AA2

## Slide 10: Approximate Adder 3
Fig.6: Approximate Adder 3
A | B | C | Sum | Carry
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 0
No. of transistors : 18
Expression:
Sum =~Carry;
Carry =(A. B)^C
[2] :M. Ramasamy, G. Narmadha and S. Deivasigamani, “Carry based approximate full adder for low power approximate computing,” 7th International Conference on Smart Computing & Communications (ICSCC), pp. 1-4, 2019.
Vdd
GND
GND
C
Vdd
Vdd
B
A
A
B
Vdd
Vdd
GND
GND
GND
Carry
Sum
Truth Table for AA3

## Slide 11
Fig.7: Approximate Adder 4
A | B | C | Sum | Carry
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 0 | 1
No. of transistors : 14
Expression:
Sum =~Carry;
Carry =AB+BC+CA
[2] :M. Ramasamy, G. Narmadha and S. Deivasigamani, “Carry based approximate full adder for low power approximate computing,” 7th International Conference on Smart Computing & Communications (ICSCC), pp. 1-4, 2019.
C
A
B
C
A
B
Vdd
B
A
B
C
C
A
GND
GND
GND
Vdd
Carry
Sum
GND
Truth Table for AA4
Approximate Adder 4

## Slide 12
Fig.8: Approximate Adder 5
A | B | C | Sum | Carry
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
[3] :V. Gupta, D. Mohapatra, A. Raghu Nathan, and K. Roy, “Low-power digital signal processing using approximate adders,” IEEE Trans. OnComputer-Aided Design of Integrated Circuits and Systems, vol. 32,no. 1, pp. 124–137, Jan. 2013.
No. of Transistors: 16
Expression:
Sum = ABC+ C
Carry = ABC +AB ++ AC+ B
Truth Table for AA5
Approximate Adder 5

## Slide 13
Fig.9: Approximate Adder 6
A | B | C | Sum | Carry
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 0 | 1
[3] :V. Gupta, D. Mohapatra, A. Raghu Nathan, and K. Roy, “Low-power digital signal processing using approximate adders,” IEEE Trans. OnComputer-Aided Design of Integrated Circuits and Systems, vol. 32,no. 1, pp. 124–137, Jan. 2013.
No. of transistors: 16
Expression:
Sum =
Carry= AB++ AC
Carry’
GND
Vdd
B
A
A
A
B
A
B
GND
C
GND
Sum
Vdd
Vdd
B
Truth Table for AA6
Approximate Adder 6

## Slide 14
Fig.10: Approximate Adder 7
A | B | C | Sum | Carry
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 0 | 1
[3] :V. Gupta, D. Mohapatra, A. Raghu Nathan, and K. Roy, “Low-power digital signal processing using approximate adders,” IEEE Trans. OnComputer-Aided Design of Integrated Circuits and Systems, vol. 32,no. 1, pp. 124–137, Jan. 2013.
No. of transistors: 13
Expression:
Sum =
Carry = ABC+AB ++ AC+ B
Sum
Vdd
GND
Carry’
GND
Vdd
B
A
C
A
B
Vdd
GND
B
Truth Table for AA7
Approximate Adder 7

## Slide 15
Fig.11: Approximate Adder 8
A | B | C | Sum | Carry
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
[3] V. Gupta, D. Mohapatra, A. Raghu Nathan, and K. Roy, “Low-power digital signal processing using approximate adders,” IEEE Trans. OnComputer-Aided Design of Integrated Circuits and Systems, vol. 32,no. 1, pp. 124–137, Jan. 2013.
No. of transistors: 11
Expression:
Sum= + + ABC
Carry = A
Carry’
GND
GND
GND
B
Vdd
A
A
C
C
A
B
Sum’
C
Vdd
Truth Table for AA8
Approximate Adder 8

## Slide 16
Fig.14: Approximate Adder 11
A | B | C | Sum | Carry
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 1
[4]: Bhargav, A.; Huynh, P. Design and Analysis of Low-Power and High Speed Approximate Adders Using CNFETs. Sensors 2021, 21, 8203
Truth Table for AA11
Approximate Adder 9
No. of transistors : 13
Expression:
Sum =
Carry =(A+BC)+

## Slide 17
Fig.15: Approximate Adder 12
A | B | C | Sum | Carry
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 1
[4]: Bhargav, A.; Huynh, P. Design and Analysis of Low-Power and High Speed Approximate Adders Using CNFETs. Sensors 2021, 21, 8203
Truth Table for AA12
Approximate Adder 10
No. of transistors : 10
Expression:
Sum =
Carry =

## Slide 18
Fig.18: Proposed AA3
A | B | C | Sum | Carry
0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 0
No .of transistors : 8
Expression:
Sum= (B^C)+ABC
Carry = BC++A+A
PROPOPSED APPROXIMATE ADDER 1
Truth Table for Proposed AA
B
A
GND
A
B
C
Sum
GND
Vdd
Carry

## Slide 19
Fig.17: Proposed AA2
A | B | C | Sum | Carry
0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 0 | 1
No .of transistors : 8
Expression:
Sum= A + (B^C)
Carry =AB+BC+CA+
PROPOPSED APPROXIMATE ADDER 2
Truth Table for Proposed AA
B
A
GND
A
B
C
Suma
GND
Vdd
Carry

## Slide 20
Fig.16: Proposed AA
A | B | C | Sum | Carry
0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 0
No .of transistors : 8
Expression:
Sum= A(B C) + (B^C)
Carry = A(B^C) + (B C)
PROPOPSED APPROXIMATE ADDER 3
Truth Table for Proposed AA
A
B
B
B
B
X
C
X
C
Sum
Carry
C
C
.
.

## Slide 21
S.No | Approximate Adder | No. of Transistors | No. of Errors |  | Technology used
 |  |  | Sum | Carry | 
1 | Exact Adder | 24 | 0 | 0 | CNTFET32nm
2 | AA1 | 14 | 3 | 1 | CNTFET32nm
3 | AA2 | 14 | 3 | 0 | CNTFET32nm
4 | AA3 | 18 | 2 | 2 | CNTFET32nm
5 | AA4 | 14 | 2 | 0 | CNTFET32nm
6 | AA5 | 16 | 2 | 1 | CNTFET32nm
7 | AA6 | 16 | 2 | 0 | CNTFET32nm
8 | AA7 | 13 | 3 | 1 | CNTFET32nm
9 | AA8 | 11 | 3 | 2 | CNTFET32nm
10 | AA9 | 13 | 2 | 0 | CNTFET32nm
11 | AA10 | 10 | 2 | 0 | CNTFET32nm
12 | Proposed AA1 | 8 | 1 | 3 | CNTFET32nm
13 | Proposed AA2 | 8 | 0 | 2 | CNTFET32nm
14 | Proposed AA3 | 8 | 1 | 1 | CNTFET32nm
21
Table 1. Summary of Approximate Adders

## Slide 22: Simulation Results of Approximate Adders
e approximate
S. No. | Adders | No. of Transistors | Delay(ns) | Power(uw) | PDP(fJ)
1 | AA1 | 14 | 1.005 | 0.1175 | 0.1180
2 | AA2 | 14 | 1.498 | 0.1569 | 0.2350
3 | AA3 | 18 | 1.006 | 9.759 | 9.8175
4 | AA4 | 14 | 1.005 | 0.1253 | 0.1261
5 | AA5 | 16 | 1.002 | 0.1244 | 0.1246
6 | AA6 | 16 | 1.006 | 0.1218 | 0.1225
7 | AA7 | 13 | 0.996 | 0.1165 | 0.1160
8 | AA8 | 11 | 1.504 | 0.1589 | 0.2389
9 | AA9 | 13 | 1.004 | 1.447 | 1.4527
10 | AA10 | 10 | 1.497 | 1.571 | 2.3517
11 | Proposed AA1 | 8 | 0.996 | 0.1339 | 0.1336
12 | Proposed AA2 | 8 | 1.495 | 0.1239 | 0.1852
13 | Proposed AA3 | 8 | 1.499 | 0.0648 | 0.0971
Table 2. Transistor count, Delay, Power and PDP of AA

## Slide 23: 4-Bit Ripple Carry Adder
The circuit diagram of 4-bit ripple carry adder is shown below
Fig.18: 4-bit ripple carry adder
PROPOSED
AA0
C0
A0
B0
C1
Sum0
PROPOSED
AA1
A1
B1
C2
Sum1
EXACT
FA0
A2
B2
C3
Sum2
EXACT
FA1
A3
B3
Carry
Sum3
[5] W. Yang, L. Wang and K. Li, "An Approximate Adder Design Based on Inexact Full Adders," 2021 IEEE 15th International Conference on Anti-counterfeiting, Security, and Identification (ASID), 2021, pp. 154-158, doi: 10.1109/ASID52932.2021.9651713.

## Slide 24: Output Waveform of 4-bit Approx. RCA
The following figure shows the transient response of proposed AA3 when it is implemented in 4-bit RCA
Fig.19: Transient response of 4-bit Approx. RCA

## Slide 25: Simulation Results of Approx. RCA
S.No | RCA | Using AA# | No.of Transistors | Delay(ns) | Power(nw) | PDP(fJ)
1 | RCA1 | AA1 | 48 | 4.00517 | 364.0 | 1.45788
2 | RCA2 | AA2 | 48 | 4.00517 | 452.6 | 1.81273
3 | RCA3 | AA3 | 56 | 4.00517 | 16630 | 0.66605
4 | RCA4 | AA4 | 52 | 4.00517 | 2380 | 9.24393
5 | RCA5 | AA5 | 60 | 4.00517 | 445.2 | 1.78310
6 | RCA6 | AA6 | 52 | 4.00517 | 377.8 | 1.51315
7 | RCA7 | AA7 | 46 | 4.00517 | 295.2 | 1.18232
8 | RCA8 | AA8 | 50 | 4.00517 | 415.4 | 1.66374
9 | RCA9 | AA9 | 54 | 4.00517 | 483.3 | 1.93770
10 | RCA10 | AA10 | 40 | 4.00517 | 232.7 | 0.93200
11 | RCA11 | Proposed AA1 | 40 | 4.00517 | 211.4 | 0.84669
12 | RCA12 | Proposed AA2 | 40 | 4.00517 | 318.0 | 1.27364
13 | RCA13 | Proposed AA3 | 40 | 4.00517 | 169.4 | 0.67847
Table 3. Transistor count, Delay, Power and PDP of Approx. RCA

## Slide 26: 2*4 Multiplier
The 2*4 multiplier has 6 inputs named a0,a1,a2,a3,b0 and b1 and has 6 outputs R0 to R7. The MA2 block is a combination of multiplier, full adder and sum block. MA1 block consists of multiplier, half adder and sum block. The outputs R2 and R3 are the outputs of the approximate adders.
a3
a0
R0
R1
R2
FA
MA1
MA2
MA2
MA2
AFA
AFA
FA
M
M
M
M
R5
R4
R3
a1
a2
b1
b0
Fig 20. Block diagram of 2*4 Approx. Multiplier
[6] Rahmati, Saeed & Farshidi, E. & Ganji, Jabbar. (2021). Low energy and area efficient quaternary multiplier with carbon nanotube field effect transistors. ETRI Journal. 43. 10.4218/etrij.2020-0045.

## Slide 27: Output Waveforms of 2*4 Multiplier
Fig 22. Transient responses of Exact and Approximate Multiplier

## Slide 28: Simulation Results of Approx. Multiplier
S.No | Multiplier | Using AA# | No. of Errors |  | Delay(uS) | Power(uW) | PDP(nW)
 |  |  | Sum | Carry |  |  | 
1 | Approx.Multiplier1 | AA1 | 3 | 1 | 2.00650 | 128.1 | 0.257032
2 | Approx.Multiplier2 | AA2 | 3 | 0 | 2.00355 | 140.3 | 0.281098
3 | Approx.Multiplier3 | AA3 | 2 | 2 | 2.00681 | 128.6 | 0.258075
4 | Approx.Multiplier4 | AA4 | 2 | 0 | 2.00665 | 131.7 | 0.264275
5 | Approx.Multiplier5 | AA5 | 2 | 1 | 2.00667 | 134.7 | 0.270299
6 | Approx.Multiplier6 | AA6 | 2 | 0 | 2.00619 | 138.4 | 0.277656
7 | Approx.Multiplier7 | AA7 | 3 | 1 | 2.00670 | 134.8 | 0.270503
8 | Approx.Multiplier8 | AA8 | 3 | 2 | 2.00660 | 128.8 | 0.258450
9 | Approx.Multiplier9 | AA9 | 2 | 0 | 2.00682 | 129.6 | 0.260084
10 | Approx.Multiplier10 | AA10 | 2 | 0 | 2.00350 | 131 | 0.262850
11 | Approx.Multiplier11 | Proposed AA1 | 1 | 3 | 2.05250 | 135.4 | 0.277908
12 | Approx.Multiplier12 | Proposed AA2 | 1 | 1 | 2.00355 | 135.7 | 0.271883
13 | Approx.Multiplier13 | Proposed AA3 | 0 | 2 | 2.00355 | 130 | 0.260461
Table 4. Error count, Delay, Power and PDP of Approx. Multiplier

## Slide 29: CONCLUSION
Three approximate full adders are designed with less number of transistors compared to the existing circuits. The proposed AA1 has less delay and proposed AA3 has low power dissipation and has less PDP. By comparing all the proposed approximate adders, the proposed AA3 is the most energy efficient circuit. So, proposed AA3 is used to implement the applications 4-bit RCA and 2*4 multiplier.

## Slide 30: PUBLICATIONS
Submitted a Springer conference paper named “Energy-Efficient Approximate Adders Using CNTFET” to International Conference on Microelectronics Electromagnetics and Telecommunications (ICMEET-2022) conducted by Sri Vishnu Engineering College for Women’s, Bhimavaram.
A Journal Paper “Low Power and Energy Efficient Approximate Full Adders for RCA and Multiplier Applications” has to be Submitted.

## Slide 31: References
[1] Bhargav, A.; Huynh, P. Design and Analysis of Low-Power and High Speed Approximate Adders Using CNFETs. Sensors 2021, 21, 8203
[2] W. Yang, L. Wang and K. Li, "An Approximate Adder Design Based on Inexact Full Adders," 2021 IEEE 15th International Conference on Anti-counterfeiting, Security, and Identification (ASID), 2021, pp. 154-158, doi: 10.1109/ASID52932.2021.9651713.
[3] G. Ferreira, P. T. L. Pereira, G. Paim, E. Costa and S. Bampi, "A Power-Efficient FFT Hardware Architecture Exploiting Approximate Adders," 2021 IEEE 12th Latin America Symposium on Circuits and System (LASCAS), 2021, pp. 1-4, doi: 10.1109/LASCAS51355.2021.9667154.
[4] W. Yang, L. Wang and K. Li, "An Approximate Adder Design Based on Inexact Full Adders," 2021 IEEE 15th International Conference on Anti-counterfeiting, Security, and Identification (ASID), 2021, pp. 154-158, doi: 10.1109/ASID52932.2021.9651713.
[5] Zahoor, Furqan, Fawnizu A. Hussin, Farooq A. Khanday, Mohamad R. Ahmad, Illani Mohd Nawi, Chia Y. Ooi, and Fakhrul Z. Rokhani. 2021. "Carbon Nanotube Field Effect Transistor (CNTFET) and Resistive Random Access Memory (RRAM) Based Ternary Combinational Logic Circuits" Electronics 10, no. 1: 79.
[6] Y. Shanmugam, S. Chandran, C. Rohith and R. Silambarasan, "Design and Analysis of Approximate Adders Using Multiplexer," 2021 7th International Conference on Advanced Computing and Communication Systems (ICACCS), 2021, pp. 977-980, doi: 10.1109/ICACCS51430.2021.9441853.

## Slide 32: Contd…
[7] Rahmati, Saeed & Farshidi, E. & Ganji, Jabbar. (2021). Low energy and area efficient quaternary multiplier with carbon nanotube field effect transistors. ETRI Journal. 43. 10.4218/etrij.2020-0045.
[8] M. Ramasamy, G. Narmadha and S. Deivasigamani, “Carry based approximate full adder for low power approximate computing,” 7th International Conference on Smart Computing & Communications (ICSCC), pp. 1-4, 2019.
[9] Ghorbani, Ali & Ghorbani, Ghazaleh. (2014). Energy Efficient Full Adder Cell Design With Using Carbon Nanotube Field Effect Transistors In 32 Nanometer Technology. International Journal of VLSI Design & Communication Systems. 5. 10.5121/vlsic.2014.5501.
[10] V. Gupta, D. Mohapatra, A. Raghu Nathan, and K. Roy, “Low-power digital signal processing using approximate adders,” IEEE Trans. OnComputer-Aided Design of Integrated Circuits and Systems, vol. 32,no. 1, pp. 124–137, Jan. 2013.
[11] V. Gupta, D. Mohapatra, S. P. Park, A. Raghunathan and K. Roy, “IMPACT: IMPrecise adders for low-power approximate computing,” IEEE/ACM International Symposium on Low Power Electronics and Design, Fukuoka, 2011, pp. 4